Raspberry Pi 4 – System Setup

# Introduction
This document describes how to setup a Raspberry Pi 4 for the OpcServant application.

OpcServant is the application for the Aeris and Air Quality products.

The official Raspberry Pi site https://www.raspberrypi.com has the Raspberry Pi documentation.

This process should have to be done once for each version, to generate a reference image. Duplicate as required using the Raspberry Pi SD Copier application. The Raspberry Pi 4 is able to provide the environment to develop and build all the libraries and application.

Using a USB thumb drive is better than an SD card as it is expected to be more robust.

The steps have the following phases:

Install the operating system
Basic system settings
Install packages
Install Node Red
Install non-standard libraries (bespoke build)
Install /usr/local libraries
Install OpcServant

# Installing Operating System

Install the operating system on a USB 3 thumb drive or a SD Micro card. A minimum capacity of 32 GB should be used. It is possible to use a SSD drive with a USB interface.

Use the Raspberry Pi Imager to write the Raspberry Pi OS on to the USB Stick or SD card.

It may be necessary to install the OS on to an SD Card in the first instance. The Raspberry Pi’s EEPROM may need editing in order to enable USB booting, see : (https://www.raspberrystreet.com/learn/how-to-boot-raspberrypi-from-usb-ssd) so booting from SD Card first is required to edit the EEPROM.

# Boot the OS
1. Power off the Raspberry Pi
2. Insert the USB Stick or SD Card into the Raspberry Pi
3. Attach monitor, keyboard and mouse
4. Connect to a wired network with Internet accesss.
5. Power On
6. When the OS has booted, change, when prompted, the password to a standard one (to be changed later)
7. Skip updates
8. Select from the menu “Preferences” → “Raspberry Pi Configuration”
9. Change the Hostname to something useful such as “Aeris_v1_1” or “AQS2_0”
10. Enable in “Interfaces”, “SSH”, “SPI” and “I2C”
11. Click OK to save the configuration
12. Reboot

# Update and Upgrade
Open a terminal window

Run the following commands:

sudo apt update
sudo apt upgrade

These usually take some time to complete.

# Install Packages

The first step is to install the Synaptic package manager

sudo apt get install synaptic

From the menu select “Preferences” → “Synaptic Package Manager”

The names of the following packages may change with the package version numbers.

Use sudo apt install <package name>

libboost-all-dev
perl
libnet-ssleay-perl
openssl
libauthen-pam-perl
libpam-runtime
libio-pty-perl
apt-show-versions
python
libgraphicsmagick
libgraphicsmagick++
libhpdf-dev
qtcreator
qt5-default
autoconf
cmake
cmake-curses-gui
cmake-extras
extra-cmake-modules
libsqlite3-dev
sqlitebrowser
minicom
libmariadbclient-dev
libcjson-dev
libssl-dev
xsltproc
libgtk3-dev
libsoup-dev
libsdl2-dev
gstreamer-dev
libmodbus-dev
libfcgi-dev

# Udev Rules For Sensor Mainboard
To fix the device name of a mainboard usb interface add rules (/etc/udev/rules.d) of this type:
SUBSYSTEM=="tty", ATTRS{idVendor}=="04d8", ATTRS{idProduct}=="00df",ATTRS{serial}=="0006900382" SYMLINK+="ttyFixedA"
The serial number can be programmed into the mainboard USB (MCP2200) and so differentiated.
# Real Time Clock
The RTC is the DS3231
Full notes here: https://pimylifeup.com/raspberry-pi-rtc/
1. To do this, we will first have to modify the Raspberry Pi’s boot configuration file so that the correct Kernel driver for our RTC circuit will be successfully loaded in.
Run the following command on your Raspberry PI to begin editing the /boot/config.txt file.
sudo nano /boot/config.txt
2. Within this file, you will want to add one of the following lines to the bottom of the file, make sure you use the correct one for the RTC Chip you are using. In our case, we are using a DS3231.
DS3231
dtoverlay=i2c-rtc,ds3231
Once you have added the correct line for your device to the bottom of the file you can save and quit out of it by pressing Ctrl + X, then Y and then Enter.
3. With that change made we need to restart the Raspberry Pi, so it loads in the latest configuration changes.
Remove the fake RTC:
sudo apt-get -y remove fake-hwclock
sudo update-rc.d -f fake-hwclock remove
sudo nano /lib/udev/hwclock-set
Find and comment out:
if [ -e /run/systemd/system ] ; then
exit 0
fi

# Webmin

Webmin (webmin.com) is a web based system administration suite. Once installed access to the display is unnecessary and targets can run entirely headless.

Copy webmin_1.980_all.deb to the target

Run:

sudo dpkg --install webmin_1.920_all.deb

# Watchdog
To enable the hardware watchdog on the Raspberry Pi:

Add to /boot/config.txt :

dtparam=watchdog=on

Configure /etc/watchdog.conf :

watchdog-device = /dev/watchdog
watchdog-timeout = 15
max-load-1 = 24

Enable the watchdog service:

sudo systemctl enable watchdog
sudo systemctl start watchdog
sudo systemctl status watchdog

# Node Red
Refer to nodered.org for details on how to install Node Red onto a Raspberry Pi.
After installation make Node Red a service:
sudo systemctl enable nodered.service

There are some MRL developed SCADA type nodes that can be added to node red.
Copy the source to the target and use npm install to add them to Node Red.
Use the Node Red palette manager to add the dash board and SVG nodes.
# Building libraries From Source
Some libraries have to be built from source. Either because the libraries are not in the repositories or because the version in the repositories is out of date. These can be found here:
Mosquitto (https://github.com/eclipse/mosquitto.git)
These can be cross compiled:
Wt (https://www.webtoolkit.eu/wt)
wxWidgets (https://www.wxwidgets.org/)
open62541 (https://github.com/open62541/open62541.git)
open62541cpp (git@github.com:bazza2jw/open62541Cpp.git)
These libraries can be built on the target. Delete the sources before releasing the disc images for production.
# Building Application From Source
The build process is as follows:
Checkout the release version from Git. This should be from GitHub. (git@github.com:We-Care-4-Air/OpcServant.git). Checkout the release branch.
The application is built using cmake. Using Qt Creator (an IDE) load the cmake file, clean and build. Change the project settings to include the install step. Alternatively go to the directory with the Cmakefile.txt, create a sub-directory (e.g. build), change to this directory and run:
cmake ..
make clean
make -j 8 install
The application can be built by cross- compilation or on the target. The former is much faster but requires the creation of a sysroot.
## Sysroot Creation
The sysroot is the set of include files and libraries for the target used during cross-compilation.
The following script will copy the files from the target to the cross compilation host:
mkdir sysroot sysroot/usr sysroot/opt
rsync -avz pi@Raspi4c:/lib sysroot
rsync -avz pi@Raspi4c:/usr/include sysroot/usr
rsync -avz pi@Raspi4c:/usr/lib sysroot/usr
rsync -avz pi@Raspi4c:/usr/local/lib sysroot/usr/local
rsync -avz pi@Raspi4c:/usr/local/include sysroot/usr/local
rsync -avz pi@Raspi4c:/opt/vc sysroot/opt
Change pi@Raspi4c to what the target is.
The script can be run to update the libraries between target and host.
Use symlink to change absolute links to relative links.
It may be necessary to manually change or add links to get a build to complete.

## Cross Compiling
To cross compile the OpcServant application the ARM cross-compiler tool chain package must be installed.
So the cross compilation links to the correct libraries and uses the correct system headers the cross compiler include and library must be remapped to the sysroot versions. If this not done the application will not execute due to library mismatches.
Goto /usr/arm-linux-gnueabihf. Rename include to include.org. Rename lib to lib.org.
Symbolically link <sysroot>/usr/include to include (<sysroot> is the path to the sysroot)
Symbolically link <sysroot>/usr/lib/arm-linux-gnueabihf to lib.
Now change to the include directory and make the following link
ln -s ./arm-linux-gnueabihf/c++/8/bits bits (where version 8 of the cross compiler is used)

In the OpcServant directory with the cmake file create a subdirectory (eg pibuild)
Change to this subdirectory
For a debug build run the command:
cmake .. -DCMAKE_TOOLCHAIN_FILE=rpi.cmake -DCMAKE_BUILD_TYPE=Debug
For a release build:
cmake .. -DCMAKE_TOOLCHAIN_FILE=rpi.cmake -DCMAKE_BUILD_TYPE=Release
Then
make clean
make -j 32 install
The -j argument sets the number of cores to use. Set this to the number of cores available on the host. The Raspberry pi has four cores.
The application is installed into the sysroot. The built files can be copied to the target.
# Runtime Files
Copy the directories under the RunTime directory to the install target directory.
# Autostarting Application
After your desktop environment starts (LXDE-pi, in this case), it runs whatever commands it finds in the profile's autostart script, which is located at /home/pi/.config/lxsession/LXDE-pi/autostart for our Raspberry Pi. Note that the directory pi might be different if you created a new user for your Raspberry Pi. If no user autostart script is found, Linux will run the global /etc/xdg/lxsession/LXDE-pi/autostart script instead.
In addition to running commands in autostart, Linux will also look for and execute .desktop scripts found in /home/pi/.config/autostart. The easiest way to execute GUI programs on boot is to create one of these .desktop scripts.
### Create a .desktop File
You do not need root-level access to modify your profile's (user's) autostart and .desktop files. In fact, it is recommended that you do not use sudo, as you may affect the permissions of the file (e.g. the file would be owned by root) and make them unable to be executed by autostart (which has user-level permissions).

Open a terminal, and execute the following commands to create an autostart directory (if one does not already exist) and edit a .desktop file :
mkdir /home/pi/.config/autostart
nano /home/pi/.config/autostart/aeris.desktop
Copy in the following text into the aeris.desktop file. Change the Name and Exec variables to your particular application.
[Desktop Entry]
Type=Application
Name=Aeris
Exec=/usr/local/MRL5/OpcServant/bin/Servant

# Release
Once the application has been built installed and tested delete all sources from the image.
Under the install directory, from the subdirectory data delete the LOCAL.db and CONFIG.DB files.
Delete any files and directories in data/reports
Ensure the directories under /home/pi are clear (not those starting with a “.”).